## Slide 1
Embedded Audio Mine
2026-06-10 found projects
Five embedded-audio candidates mined for firmware, hardware, DSP and adaptation value.
RP2350
MOD2
Daisy
PENDAII
PSX
Verb
Spectral
Delay
Pedal
Proto
Patterns
+ Steps
Embedded Audio Mine • 2026-06-10
01

## Slide 2
Digest map
Ranked by utility × novelty × adaptability, with hardware evidence boosted.
1
modulove/MOD2
STRONG_PASS
RP2350 Eurorack firmware personalities + UF2
RP2350 / XIAO
2
PENDAII hardware + software
PASS
Stereo Daisy pedal platform: KiCad + framework
Daisy Seed
3
CVCHothouse: PSXVerb
PASS
PlayStation SPU reverb model on Hothouse
Daisy / Hothouse
4
FuzzyLotus/Phantasmagoria
STRONG_PASS
Flashable spectral delay for Terrarium/Daisy
Daisy / Terrarium
5
Daisy Effect Pedal Prototyping Board
REF_PASS
Forum-hidden pedal hardware scaffold
Daisy + Oopsy
What to mine: release packaging • hardware/service boundaries • authentic DSP constraints • UI/control models • first-step adaptation paths
Embedded Audio Mine • 2026-06-10
02

## Slide 3
Project landscape
The five finds cover three useful adaptation routes: voice firmware, pedal platform, and DSP algorithm.
Route
Candidate
Reusable asset
First payoff
Firmware voices
MOD2
UF2 + source personalities
Best direct flash path
Hardware platform
PENDAII
KiCad + Daisy framework
Best carrier-board reference
Algorithm model
PSXVerb
SPU reverb memory/rate model
Best DSP study
Effect product
Phantasmagoria
Spectral delay + release binary
Best immediate pedal experiment
Hardware scaffold
Pedal protoboard
Gerber/BOM/forum workflow
Best bench-proto clue
Bias: hardware+firmware wins when evidence is comparable. Firmware-only can still outrank if it is flashable and reusable immediately.
Embedded Audio Mine • 2026-06-10
03

## Slide 4
1 • modulove/MOD2
RP2350/XIAO Eurorack firmware ecosystem with UF2 deployment.
STRONG_PASS
RP2350
UF2
BOOTSEL
UF2 drop
XIAO
RP2350
MOD2
controls
Voice
engine
PWM
audio
Firmware personalities
• BRAIDS macro oscillator • CLAP / CLAVES / FM_DRUM • HIHAT / KICK / VCO
Engineering value
• Immediate flash path • Compact control mapping • Multi-personality module model
Main caveat
• PWM output needs filtering • Hardware details partly external • Per-firmware licenses differ
Adaptation target: port one voice to Pico 2 + external I2S DAC, then package as UF2 for quick iteration.
Embedded Audio Mine • 2026-06-10
04

## Slide 5
2 • PENDAII hardware + software
Stereo Daisy Seed pedal platform: KiCad hardware meets reusable firmware services.
PASS
Daisy Seed
KiCad 9
Stereo pedal
Audio I/O
+ dry path
Codec
framework
Daisy Seed
DSP core
UI
ST7789 + enc
MIDI
+ presets
Hardware evidence
• KiCad project + PCB • PDF schematic + fabrication folder • Audio / power / UI sub-schematics
Software services
• Codec init + real-time processing • SDRAM / QSPI persistence • DaisySeedGFX2 + PendaUI
Design lesson
• Separate platform services from effect code • Analog dry path lowers failure risk • Good basis for custom carrier
First inspection step: open Audio_sch + pin spreadsheet; verify codec, dry/wet topology, gain staging, grounding and display/encoder mapping.
Embedded Audio Mine • 2026-06-10
05

## Slide 6
3 • CVCHothouse: PSXVerb
A constrained DSP reverb study: PlayStation SPU behavior rebuilt on Daisy/Hothouse.
PASS
Daisy / Hothouse
24 kHz core
sub-ms dry path
48 kHz
I/O
Halfband
decimate
24 kHz
SPU core
Circular
int16 memory
Halfband
interpolate
Reusable DSP idea
• Rate conversion as character • Saturation + memory model • Preset-specific work areas
Implementation clues
• 39-tap halfband FIR • 4-sample audio block • ~62 kB largest work buffer
Caveat
• Hothouse mapping required • License split needs care • Algorithm-first, not full product
Best next move: extract the core and wrap it in a minimal Daisy Field UI to visualize preset memory, mix, feedback and aliasing behavior.
Embedded Audio Mine • 2026-06-10
06

## Slide 7
4 • FuzzyLotus/Phantasmagoria
Flashable spectral delay for PedalPCB Terrarium / Daisy Seed.
STRONG_PASS
Daisy Seed
Terrarium
Release binary
Control model
• Reverse + freeze behavior • Warble / room / halo / evolution switches • Delay texture aimed at experimental pedal use • Build-from-source path plus binary release
Signal idea
Input
Spectral
delay
Freeze
reverse
Output
Engineering read
• Best immediate pedal experiment • Good UI mapping study • Less hardware-rich than PENDAII • Worth testing on Terrarium/Hothouse-like carrier
First step: flash the released binary, then compare live control behavior before spending time reading the DSP core.
Embedded Audio Mine • 2026-06-10
07

## Slide 8
5 • Daisy Effect Pedal Prototyping Board
Forum-hidden bench PCB scaffold for Daisy pedal experiments.
REF_PASS
Daisy forum
Gerber/BOM
Oopsy/Max flow
Hardware scaffold
• Terrarium-like prototyping board • Buffered audio path • 9 V pedal-style input • Daisy DAC/LED headers
Why keep it
• Not polished, but practical • Forum context exposes real bring-up flow • Good carrier-board comparison point • Useful for quick Oopsy patches
Why not higher
• Forum attachment evidence • Source depth limited • Needs schematic/net review • Better as reference than product
Bench board
Oopsy / Max patch
Fast pedal prototype
Embedded Audio Mine • 2026-06-10
08

## Slide 9
Cross-project engineering patterns
What is worth stealing from the whole set.
Flashable distribution
MOD2 and Phantasmagoria reduce friction with UF2/binaries. Package future projects this way.
Hardware/service split
PENDAII cleanly separates carrier-board services from the effect layer.
Constrained DSP character
PSXVerb shows rate conversion, saturation and circular memory as deliberate sound design.
Forum-hidden hardware
Pedal protoboard is weak as a product but useful as a quick carrier-board comparator.
Control discipline
Small control surfaces force clear parameter grouping: pots, switches, encoders, MIDI, presets.
Practical bias: start with immediate flash tests, then inspect hardware nets before copying analog/audio sections.
Embedded Audio Mine • 2026-06-10
09

## Slide 10
Recommended first passes
Fast way to convert the digest into useful engineering work.
30 min
Flash / run
MOD2 UF2 or Phantasmagoria binary. Verify audio path before code reading.
60 min
Schematic audit
Open PENDAII Audio + power sheets. Identify codec, gain, dry/wet and grounding decisions.
90 min
DSP extraction
Lift PSXVerb core into a minimal host. Measure buffer, CPU, latency and saturation behavior.
Half day
Carrier comparison
Compare PENDAII vs Terrarium/Hothouse/protoboard: controls, MIDI, display, bypass, serviceability.
Later
Own platform
Pick one architecture: RP2350 voice module or Daisy stereo pedal carrier. Package as release-first firmware.
Do not commit tracker rows until the digest Markdown is actually written to the repository.
Embedded Audio Mine • 2026-06-10
10

## Slide 11
Source links and tracker context
Deck derived from the 2026-06-10 digest artifact. Links are included for inspection.
modulove/MOD2
https://github.com/modulove/MOD2
PENDAII-Hardware
https://github.com/DADDesign-Projects/PENDAII-Hardware
PENDAII-Software
https://github.com/DADDesign-Projects/PENDAII-Software
CVCHothouse / PSXVerb
https://github.com/charlesvestal/CVCHothouse
Phantasmagoria
https://github.com/FuzzyLotus/Phantasmagoria
Daisy forum pedal prototyping board
forum.electro-smith.com thread referenced in digest
Anti-repeat context
Recent tracker state blocks many Daisy/Teensy/Pico projects through July 2026; these five candidates were selected because they were not hard repeats in the inspected anti-repeat resources.
Embedded Audio Mine • 2026-06-10
11